## Slide 1: Initial Slambot Plan
Tim Ousley
Garrett Witowski

## Slide 2: Component Overview
RGBD Image Source
Landmark Identifier
Pose Estimator
SLAM
Odometry Source
Display
Frame Store

## Slide 3: Interface Overview (Nested CB’s)
RGBD Image Source
Landmark Identifier
Pose Estimator
SLAM
Odometry Source
Display
Frame Store
ResetOdometer()
Odometer GetOdometerValue()
SetFrameInterval(Float seconds)
RegisterRGBDCallback(func cb)
RGBDCallback(int ID, Image rgb, Image depth)
T GetAttribute<T>(ID, String attrName)
SetAttribute<T>(ID, String attrName, T attrValue)
PCL GetPCL(ID)
Image GetRGB(ID)
Image GetDepth(ID)
FrameCallback(…)
RegisterFrameCallback(func cb)
RegisterFrameCallback(func cb)
LandmarkCallback(…)
RegisterPoseCallback(func cb)
PoseCallback(…)
RegisterSLAMCallback(func cb)
Notes:
Nested CB’s forces 1-to-1 mapping. Is that OK?
Frame Store is getting a lot of responsibility.
  Efficient Image storage
  Get/set attributes
  Conversion to PCL
  Callback mgmt
3) It’s hard to unit test anything without Frame Store

## Slide 4: Interface Overview (CB Manager)
RGBD Image Source
Landmark Identifier
Pose Estimator
SLAM
Odometry Source
Display
Frame Store
ResetOdometer()
Odometer GetOdometer()
SetFrameInterval(Float seconds)
RegisterRGBDCallback(func cb)
RGBDCallback(int ID, Image rgb, Image depth)
T GetAttribute<T>(ID, String attrName)
SetAttribute<T>(ID, String attrName, T attrValue)
PCL GetPCL(ID)
Image GetRGB(ID)
Image GetDepth(ID)
FrameCallback(int ID)
FrameCallback(int ID)
Callback Manager
RGBDCallback(int ID, Image rgb, Image depth)
RegisterRGBDCallback(func cb)
RegisterFrameCallback(func cb, priority)
FrameCallback(int ID)
Notes:
CallbackManager makes N-to-N extensions possible
Frame Store still has a lot of responsibility.
  Efficient Image storage
  Get/set attributes
  Conversion to PCL
3) It’s hard to unit test anything without Frame Store
4) Pose Estimator can return a lot of possible poses that get trimmed in FastSLAM—it might not make sense to store that transient info in Frame Store
5) I have a bad feeling about lots of memory copies but can’t put my finger on exactly why
6) CallbackManager extensible to multiple Landmark Estimators or Pose Estimators pretty easily
Time Source
ResetTime()
Seconds GetTime()
FrameCallback(int ID)

## Slide 5: Odometry Source
Odometry Source
6 Axis summary of odometry readings from wheels (x,y,z, pitch, yaw, roll) since last reset
Initial implementation always returns 0’s
  Only slightly more complicated to linear or quadratic extrapolate new position from last two positions
SLAM can use this as a fallback if other sensors return confusing data
Could be extended to add GPS coordinates
ResetOdometer() – returns value & reset.
GetOdometer() – side effect free way to peek at the odometer
Odometer ResetOdometer()
Odometer GetOdometerValue()

## Slide 6: RGBD Image Source
Wrapper around asynchronous Kinect Image+Depth callbacks
Alternate implementation reads frames from files—makes testing easier
Decimates frames if needed
SetFrameInterval() – default 0.0, higher values enable decimation
RegisterRGBDCallback() – All registered callbacks are called for every non-decimated RGBD frame that is received
RGBD Image Source
SetFrameInterval(Float seconds)
RegisterRGBDCallback(func cb)

## Slide 7: Callback Manager
Sequences SLAM steps
Allows extensibility for new in-between steps, or alternate implementations of the same step
  Useful for testing, or for algorithm comparison/machine learning
RGBDCallback called first, then FrameCallback’s in priority order
Makes profiling easy
If processing isn’t finished on previous frame, Callback Manager will drop the new frame instead of forwarding the RGBD callback as normal
RGBDCallback() – called from any RGBD source
RegisterRGBDCallback() – allows RGBD callback to be forwarded as needed
RegisterFrameCallback() – prioritizes steps of SLAM
Callback Manager
RGBDCallback(int ID, Image rgb, Image depth)
RegisterRGBDCallback(func cb)
RegisterFrameCallback(func cb, priority)

## Slide 8: Frame Store
Stores all RGBD’s (probably in files?)
Stores all attributes (dictionary? Db?)
Converts between RGBD and PCL
  Probably should be broken up some
Initial implementation done with List<RGBD> and List<Dictionary<String, Object>>
Attribute handling should be refined some
GetAttribute<T>()/SetAttribute<T>() – intended to pass through to a dictionary for each frame
GetPCL() – return RGBD as a PCL for the frame (this should probably go elsewhere)
GetRGBD()/GetDepth() – most landmark detection works faster working with Images than PCLs
Frame Store
RGBDCallback(int ID, Image rgb, Image depth)
T GetAttribute<T>(ID, String attrName)
SetAttribute<T>(ID, String attrName, T attrValue)
PCL GetPCL(ID)
Image GetRGB(ID)
Image GetDepth(ID)

## Slide 9: Landmark Identifier
Identifies landmarks in the frame
  Lots of implementation options for what can be identified as a landmark (blob analysis for colored tags, corners, contrasty floor tiles)
  Multiple landmark identifiers may be used at same time
Landmarks added frame “landmark” attribute
Landmark data structure TBD, should include confidence!
FrameCallback() – called for each frame
Landmark Identifier
FrameCallback(int ID)

## Slide 10: Pose Estimator
Combines landmarks from current frame and previous frame to estimate pose
  Lots of trig/linear algebra to back out change in x, y, z, pitch, yaw, and roll from landmarks
  Sensor error/accuracy + distortion + odometry error mean no one solution will match all points. Instead return several probable poses
FrameCallback() – called for each frame
Pose Estimator
FrameCallback(int ID)

## Slide 11: SLAM
Selects most accurate from the available poses
Using the existing map, updates current pose and may correct errors in the map
Initial implementation blindly chooses highest confidence pose from Pose Estimator
  Will have problems if robot completes a loop, ever.
Better implementation would be FastSLAM 2.0
FrameCallback() – called for each frame
SLAM
FrameCallback(int ID)

## Slide 12: Display
Show location to user
  Current Image + Depth display from RGBD Source
  Pointcloud of nearby map + current RGBD pointcloud
No control/actuators to affect robot motion
Direct3D/OpenGL Map viewer
  Lower alpha value for older PCLs?
Other implementations possible
FrameCallback() – called for each frame. Last thing called by the Callback Manager
Display
FrameCallback(int ID)

## Slide 13: Open Design Issues
PCL conversion should be a helper class, not stored in Frame Store
Frame Store attribute system is missing common Dictionary functionality (list all keys? Is key present? Etc)
Landmark data type needs definition
How do multiple types of landmarks exist in the Frame Store? What is that data format?
Pose Estimator return type needs definition
What is the minimal possible implementation of Display?
RGBD Image Source
Landmark Identifier
Pose Estimator
SLAM
Odometry Source
Display
Frame Store
Callback Manager
Time Source